## Slide 1
BONSAI-ON-CHIP
Bonsai-on-chip
project progress
30 September 2026
Week 0 complete
Week 1 simulation passed
Physical FPGA gate remains open
Notes: Snapshot for a team meeting. Week 0 setup is complete, including a physical vendor-adder smoke test. The custom Bonsai first slice has passed simulation, but its physical FPGA gate remains open. No full-model inference or token-generation claim.
Sources:
https://github.com/Ergodex-Core/bonsai_on_chip/blob/55f5995a3cb7afee55b21937010c1da9715fa3a2/reports/ERG-102/README.md
https://github.com/Ergodex-Core/bonsai_on_chip/blob/55f5995a3cb7afee55b21937010c1da9715fa3a2/reports/ERG-103/README.md
https://linear.app/ergodex-ai/project/model-in-silcon-bonsai-2-27b-ternary-quant-f2d1c0029436

## Slide 2
BONSAI-ON-CHIP
02
Verified progress
30 Sep 2026 / Team progress update
EVIDENCE CLASS | VERIFIED RESULT | SCOPE
Week 0 native suite | 1,332 selected targets | 1,046 fresh + 286 cached
Vendor environment | 9/9 XSIM tests 2,264 F2 additions | Simulation + vendor hardware
Week 1 local first slice | 16 steps 396 native + 6 synthetic | 242,357,184 bytes Two full readback hashes
Custom F2-target XSIM | 87 explicit checks 3 real Q1 + 1 synthetic | 4,160-byte compact image
The custom Bonsai evidence covers simulation. Full-model inference remains unvalidated.
Notes: Evidence classes must stay separate. Week 0 selected target count includes cached results, not 1,332 fresh executions. The physical 2,264-addition run used the public vendor adder AFI, not the Bonsai accelerator. Week 1 16-step local validation uses source 3ee0f99eb7216fe41ba55e719584c662313d3b10. Its six synthetic cases include two expected invalid-code rejections. Full canonical image size is 242,357,184 bytes and SHA256 ccd70c080f8758e1b4df58c2fdbdd6d13bb65571abbc56feb6942de1f8c07d99. Custom XSIM source 839e5fc1729c36903843ccc03ea6742bd4a265f9 passed 87 explicit check() calls, including 65 compact image line compares, 20 checks across four jobs and two setup checks. The 4,160-byte compact smoke covers three actual 1.7B Q1_0 blocks and one synthetic ternary unit-scale block. Vendor memory models are simulation, not physical memory execution.
Sources:
https://github.com/Ergodex-Core/bonsai_on_chip/blob/55f5995a3cb7afee55b21937010c1da9715fa3a2/reports/ERG-102/README.md
https://github.com/Ergodex-Core/bonsai_on_chip/blob/55f5995a3cb7afee55b21937010c1da9715fa3a2/reports/ERG-103/README.md
https://github.com/Ergodex-Core/bonsai_on_chip/tree/839e5fc1729c36903843ccc03ea6742bd4a265f9/fpga/aws_f2/first_slice

## Slide 3
BONSAI-ON-CHIP
03
F2 execution and simulation rates
30 Sep 2026 / Team progress update
Custom XSIM and pinned SDK build passed
Synthesis and placement complete. Routing active at 17:40 UTC.
MEASURE | VALUE | INTERPRETATION
Verilator workflow | ~3.42M cycles/sec | 99,098,552 cycles / 29.017 sec
DOT128 local latency | 138–157 cycles | Per operation, excludes host work
XSIM / FPGA clock | 250 MHz / 250 MHz | Modeled clock / implementation target
Arcilator first slice | Smoke + synthetic pass | Full native run pending
Preliminary post-place setup: −0.647 ns. Final routed timing pending.
Next gates: timing/DRC, custom AFI, physical full-image run, PR review.
F2 source 839e5fc1
Notes: Hardware status as of 17:40 UTC on 30 Sep 2026, pending final refresh. Source 839e5fc1729c36903843ccc03ea6742bd4a265f9. Post-place WNS is preliminary, not a routed timing result or achieved clock. Target period 4 ns (250 MHz). Full-chip Arcilator remains unvalidated. The new first-slice Arcilator compile and link passed, followed by 3 mailbox checks, 4 protocol checks and all 6 synthetic cases. Full native runtime validation remains pending. These are interim results before the final source-bound rerun after a build-helper bounds correction. The runtime is x86_64 Linux Docker under emulation on an arm64 Mac, so its speed would not be directly comparable with the earlier native Verilator run. No measured Arcilator rate is claimed. Native AWS EC2 execution is the next preparation step, not completed evidence.
Verilator workflow rate was calculated as 99,098,552 logical core cycles / 29.017 wall seconds = 3.415189 million cycles/sec on Mac arm64. This includes native host workflow image load, two full readbacks and hashing, and 396 jobs. model_server steps logical cycles without a physical time setting. It is not a hardware frequency and not a pure compute-only simulator benchmark. DOT128 138–157-cycle latency excludes image load, control work and host scaling. XSIM uses the pinned shell's modeled 250 MHz clock. Physical accelerator frequency depends on final routed timing.
Sources:
https://github.com/Ergodex-Core/bonsai_on_chip/blob/55f5995a3cb7afee55b21937010c1da9715fa3a2/reports/ERG-103/README.md
https://github.com/Ergodex-Core/bonsai_on_chip/blob/3ee0f99eb7216fe41ba55e719584c662313d3b10/tests/first_slice/model_server.cpp
https://github.com/Ergodex-Core/bonsai_on_chip/pull/2

## Slide 4
BONSAI-ON-CHIP
04
HBM weight store and array design
30 Sep 2026 / Team progress update
HBM is the preferred FPGA ROM equivalent
Current DDR first slice is implemented. HBM and the array remain design proposals.
STORAGE CONTRACT
Load the image, verify its hash, then seal it.
Block every writer during execution. Reload after HBM reset or data loss.
INTEGRATION BOUNDARY
CoralNPU control and RVV prepare work.
A shared weight store feeds staging buffers and the proposed ternary array.
Current logical image cap: 256 MiB. A 27B design needs versioned addressing and a complete HBM budget.
Notes: Architecture proposal only. No array RTL is authorized or implemented by this design task. Current ERG-103 transport targets DDR and preserves immutable load/readback-hash/seal with logical offsets and image epoch. Preferred HBM proposal must gate every writer alias, including host, debug, scrubber and performance paths, and invalidate data on reset or loss of memory validity. ASIC ROM is a separate proposed backend. Current ABI limits logical image size to 256 MiB, so large models require a versioned interface and capacity design.
A 16 GiB HBM physical capacity does not establish that a 27B checkpoint and its runtime state fit. Official 27B header-only research found PTQ1_0 file 5,946,648,928 bytes and PQ2_0 file 7,206,168,928 bytes, publisher identities only. KV and recurrent state, activations, descriptors and reserved regions still need budgeting. Full stated max context has 16 GiB dense FP16 KV alone for batch one before weights. No model execution or fit claim.
Sources:
https://github.com/Ergodex-Core/bonsai_on_chip/blob/2537a48665a13063e733713d855647df2f325c04/doc/microarch/weightstore.md
https://github.com/Ergodex-Core/bonsai_on_chip/blob/2537a48665a13063e733713d855647df2f325c04/doc/microarch/ternary-systolic-array.md
https://huggingface.co/prism-ml/Ternary-Bonsai-2-27B-gguf/tree/b072e1d3b35a0a630cece372c2127528e0994386

## Slide 5
BONSAI-ON-CHIP
05
Next deliverables and decisions
30 Sep 2026 / Team progress update
01
Close the ERG-103 physical gate
Finish routed timing and DRC, create the custom AFI, run the full
396 + 6 fixture with image hashes, then review PR #2.
02
Freeze the 27B reference and array interfaces
Select PTQ1_0 or PQ2_0 and validate the required activation transform.
Agree the HBM context budget and interface owners before array RTL.
EACH ISSUE DELIVERS
A PR, runnable simulation, actual FPGA evidence and an attached report
Accountable: Rachit Tibrewal. Current fixture: 1.7B Q1_0 binary weights.
Notes: ERG-103 planned due date is 2 October, not a forecast of physical closure. Owner Rachit Tibrewal. PR #2 remains draft until required physical evidence and review. The current native fixture uses pinned Bonsai-1.7B-Q1_0 binary weights, not the 27B ternary candidate. No inference tokens have been generated by the custom FPGA slice.
The official candidate prism-ml/Ternary-Bonsai-2-27B-gguf is pinned to b072e1d3b35a0a630cece372c2127528e0994386. Metadata-only inspection identifies 851 tensors (402 ternary, 353 F32, 96 BF16), Qwen3.5 hybrid 64 layers (48 linear and 16 full attention), with required normalized block-1024 Hadamard activation rotation, signs and embedding inverse. PTQ1_0 or PQ2_0 format is not yet frozen. Validate against the Prism runtime and exact decoder before implementation. Publisher LFS identities are not full local file hash verification.
Sources:
https://github.com/Ergodex-Core/bonsai_on_chip/pull/2
https://linear.app/ergodex-ai/project/model-in-silcon-bonsai-2-27b-ternary-quant-f2d1c0029436
https://huggingface.co/prism-ml/Ternary-Bonsai-2-27B-gguf/tree/b072e1d3b35a0a630cece372c2127528e0994386
https://github.com/PrismML-Eng/llama.cpp/blob/adfffbe41b2cabcd51fff326ab045662265062bb/ggml/src/ggml-common.h#L199-L220
https://github.com/PrismML-Eng/Bonsai-demo#upstream-status-for-bonsai-2